- Use a good quality battery to prevent flashlight damage due to leaks and other self-destructive battery behaviors.

- Remove the batteries from the flashlight if not used for long periods of time or if the battery power has been depleted. This will help prevent battery leaks that may damage the light.

- Replace the O-Rings if they are damaged or if they show signs of wear due to extended use. Regularly add lubrication to the O-Rings to prevent erosion, this will help keep the flashlight properly sealed against water.

- Clean the electrical contacts periodically, especially if the light flickers or fails to work. A flickering or ‘dead’ light may be caused by the following reasons:

1. The battery needs to be replaced.

Solution: Replace battery, ensuring the anode side (+) faces to the head of the flashlight.

2. The threads, PCB board contact, or other contacts are dirty.

Solution: Carefully clean the threads and contact points with alcohol and a cotton swab.

3. The head, tube, or internal parts of the tailcap are loose.

Solution: Add some lubrication to the O-Rings and tightly screw in the head and tail parts.

If the above methods don’t solve your problem, please contact your local dealer.

AE LIGHT warrants our flashlights to be free from defects in workmanship and materials for 24 months of the original owner. Normal wear and tear is not covered, nor is damage resulting from misuse, abuse, neglect, battery damage, use of incorrect battery, or altering these products from their original state. Parts and accessories for flashlights are not covered by this warranty.

AE LIGHT

TEL: 541-471-8988    FAX: 541-471-2263

E-mail: led@aelight.com	 Web: http://www.aelight.com

AE LIGHT AEL460TD11

High Power Backup Flashlight

Pocket Size Variable-output

----------------------------------------------------------------------------------------

User Guide

1. Coated tempered lens resists impact. Aluminium Strike Bezel.

2. Aerospace aluminum body. Mil-Spec hard-anodized. O-ring Sealed.

3. Anti-roll design.

4. Slip-resistant body design.

5. High ductile steel removable clip.

6. Push-button tailcap switch with tail-standing design.

| LED | CREE XM-L T6 |
| --- | --- |
| Low output / runtime | 4 lumens / 80 hours |
| High output/ runtime | 460 lumens / 1.3 hour |
| Length | 3.3 inches (84mm) |
| Diameter | 0.9 inches (21.8mm) |
| Weight | 1.44 ounces (41g) |
| Battery type | 1×CR123A |

Unscrew the body or tail cap, remove the old battery and insert new battery for maximum operation time as shown:

Warning: Batteries can explode or cause burns if disassembled, shorted, recharged or exposed to fire or high temperatures. Do not expose contents to, water, mix with used or other battery types.

# Text boxes

Maintenance

Warranty

Construction

Specifications

Battery Replacement

To Control Dimming/Strobe Modes:

A. Press the tailcap switch ON/OFF to switch between 3 output modes: Low, Medium and High. The light has no memory, so its mode will reset to Low after 2 seconds off.

Flashlight Operation

B. Loosen the head to switch to Strobe mode. Press the tailcap switch ON/OFF to switch between 3 modes: Strobe, Flash and Slow Flash. The light has no memory, so its mode will reset to Strobe after 2 seconds off.