Page 1

Page 2

AEL600 Features

- Three modes of output easily accessed by pressing the end switch for High, Medium, & Low.

- Knurled body to ensure positive grip in wet locations.

- Ready for weapon mounting. The electronics in the light head and tail cap are spring mounted to absorb recoil shock. Standard 1” body diameter.

- Rated IPX-8 the AEL600 is water resistant to 5-foot depth.

- Removable grip ring, & pocket clip. Stainless Steel Crenelated Strike Bezel.

- Fully exposed Tactical rear switch for ease of activation even while wearing gloves.

- Optional remote switch for use as a weapon light

Items included in light set

1-Stainless Steel Pocket Clip

1-Lanyard

1-Spare O-ring set

1-Nylon pouch

Batteries and chargers not included and are ordered separately. 18650 or CR123

Page 3

Features

- LED: Cree XM-L LED U2 with a lifespan of 50,000hours

- Power Source: 1*18650 rechargeable battery or 2*CR123A

- Rated Operation Voltage: 2.7V-8.4V

- Max light output: 600 lumens

- Max runtime: 50hours @ low mode

- Runtime High Mode: 80 minutes for 1*18650 down to 50%. 60 minutes down to 50% (w/2*CR123A)

- 16000Lux @ 1m (3ft)

- Max beam distance: 255 Meters (850ft.)

- Peak beam intensity: 18000cd

- Impact resistance: 1.2m (48in)

- Waterproof to IPX-8 standard

- Length (mm): 184*41.5*25.4 (inch) 7.25*1.63*1

- Weight: 174g (6.14oz) (excluding batteries)

- Material: Aircraft grade aluminum

- Type 111 Hard anodizing

- Precision focused hard coated reflector

Page 4

Operation

Inserting battery(s)

Unscrew tail cap and insert 1-18650 rechargeable li-ion battery or 2-CR123 batteries, with Positive (+) terminal toward the front of the light. NOTE: if using CR123 batteries never mix used batteries with new batteries as this can cause the batteries to catch fire. Make sure both CR123 batteries face the same direction or light will overheat and batteries can catch fire.

Mode Switching

- Soft Touch Once: High

- Soft Touch Twice: Medium

- Soft Touch 3 times: Low

- Hard press to set at selected mode

- Light resets to high mode when turned off.

- For Strobe: Slightly unscrew the head light

Insert battery with Positive (+) terminal toward the head of light.

Page 5

Maintenance

Do not disassemble the sealed light head, doing so can damage the electronics and will void the warranty.

Use only high quality li-ion batteries with high capacity.

Additional high capacity batteries are available from your local dealer. If storing your flashlight, remove the battery(s) to protect against leaks that will damage your light.

A spare O-ring is included with your light. Replace the O-ring if it is damaged. Lubricating the O-ring will prolong its life and ensure proper sealing for water and dust.

Periodically clean the contacts to ensure proper operation with a cotton swab and denatured alcohol.

Make sure the threads on the tail cap are clean and be careful not to cross thread when installing the end cap.

Page 6

Warranty

AE Light warranties the flashlight to the original retail buyer against defects in material and workmanship. Flashlights that are found to be defective under normal use within 24 months of purchase date will be repaired or replaced at AE Light discretion. Batteries are not covered under this warranty. Proof of purchase required. This warranty does not cover damage cause by accident, misuse, or alteration. Failure to properly maintain your flashlight will void your warranty. Customer is responsible for shipping to and from AE LIGHT facility for warranty repair/replacement. Registration of your light is required prior to a warranty claim. The light can be registered at: www.aelight.com. When registering on line you will receive a discount coupon good toward the purchase of accessories or additional lights.

AE LIGHT

Ph: 01-541-471-8998

E-mail: HID@AELIGHT.COM

www.aelight.com

P.O. Box 1869 Rogue River, OR 97537 USA